## Slide 1
SMART INDIA HACKATHON 2026
SubsiGuard
Mine subsidence monitoring & early warning
Problem Statement ID: SIH26025
Problem Statement Title:-
Development of an AI-enabled Low Cost Real Time Mine Subsidence Monitoring, Prediction and Early Warning System for Underground Coal Mines in India.
Theme: Smart Automation
PS Category: Hardware
Team Name: MineNova6
Team ID: [To be assigned]
Notes: SubsiGuard student prototype proposal for SIH26025. Official problem-statement title and team details retained from the supplied deck. Team ID awaits assignment.

## Slide 2
TEAM
MineNova6
SubsiGuard: Surface Mesh Early Warning System
@SIH Idea submission- Template
2
❖ Proposed Solution (Describe your Idea / Solution / Prototype)
EXISTING METHODS & MONITORING GAP
Satellite InSAR: Radar works through clouds. Periodic revisit and processing cannot provide continuous local telemetry.
Optical ground surveys: Periodic field observations leave gaps between measurements and may expose surveyors to unstable ground.
Microseismic monitoring: Tracks seismic activity. Direct surface tilt and displacement sensing provides complementary deformation evidence.
Borehole extensometers: Measure movement at instrumented locations. Drilling and installation needs vary by site.
SUBSIGUARD: LOCALIZED SURFACE MESH
Continuous sensing: Surface nodes above underground coal mine panels monitor tilt, vibration, relative displacement and cracks.
Hybrid analysis: 100 Hz local sampling and filtering/features feed 1 Hz feature telemetry, Random Forest risk classes and a physics-based trend estimator.
Low-cost network: Custom multi-hop LoRa P2P mesh in India’s 865–868 MHz band, with local buffering and solar-assisted power.
Independent fail-safe: ESP32 thresholds trigger local indication. Gateway/local relay siren works without cloud. SMS/app alerts need gateway connectivity.
THE CRITICAL GAP IDENTIFIED
Continuous real-time surface deformation monitoring above underground mine panels, with localized wireless sensing and offline early warning.
Notes: Proposed design, not a demonstrated field safety system. 100 Hz is local sensor acquisition; 1 Hz feature/status telemetry is a prototype target subject to packet size, spreading factor, duty/access rules, number of hops and network load. Raw 100 Hz streams are not sent continuously over LoRa. Sources: https://www.dot.gov.in/static/uploads/2025/07/84f33f09e137fa81930f44bcd5f2d238.pdf
https://www.isro.gov.in/ISRO_EN/PSLVC56_DS_SAR_Mission.html?timeline=timeline

## Slide 3
TEAM
MineNova6
TECHNICAL APPROACH
@SIH Idea submission- Template
3
❖ Technologies to be used & Process Workflow Architecture
1. SURFACE SENSOR PROTOTYPE
ESP32 node: MPU-6050 tilt/vibration and wired linear displacement sensor.
Relative movement: Anchored node-pair baselines or cracks. LoRa RSSI is not a displacement measure.
Calibration: Prototype tilt accuracy and displacement resolution require validation.
2. HYBRID RISK ANALYSIS
Random Forest: Normal / Warning / Critical from deformation features.
Inverse velocity: Probable failure trend/window only with a sustained acceleration trend.
Prototype ML data: Controlled/simulated scenarios. Real mine data and field calibration required.
3. SPATIAL MODEL & LOCAL SAFETY
Knothe model: Physics-informed spatial/calibration layer. Configurable geometry and strata.
Offline GIS: Local maps and data storage. Sync when connectivity returns.
ESP32 thresholds: Independent node/gateway alarm path bypasses ML, backend and cloud.
SURFACE MONITORING WORKFLOW
SURFACE NODES
Tilt • vibration
Displacement • cracks
ESP32 LOCAL SENSING
100 Hz sampling
Filtering + features
LoRa P2P MESH
Custom multi-hop
865–868 MHz
LOCAL GATEWAY
Feature ingestion
Buffer + local database
1 Hz feature/status telemetry target
Scheduling/retries subject to mesh airtime and WPC limits
RANDOM FOREST
Normal / Warning / Critical
INVERSE-VELOCITY
Displacement trend
Probable window
with uncertainty
GIS / DASHBOARD
Live risk zones + history
Local siren is primary
SMS/app: connected only
Gateway runs both models
and retains local history
INDEPENDENT ESP32 THRESHOLD FAIL-SAFE
Node threshold → local buzzer / LED
Gateway threshold → local relay / siren
Runs without ML, backend or cloud decisions
Node indication remains available during mesh/gateway outage. Gateway siren needs a working local link.
Notes: Sensor nodes are on the surface above underground coal mine panels. A wired extensometer/string potentiometer across selected anchored point pairs measures relative displacement; RSSI is only a radio-link indicator. Anti-alias filtering and calibrated sensor bandwidth must match the sampling rate. Train/test Random Forest on separate controlled/simulated runs to avoid leakage, then validate false positives/negatives on mine data. Saito creep forecasting and Fukuzono inverse velocity are physics-based methods originally investigated for slopes; transfer to mine subsidence is a hypothesis requiring field validation. Show no failure window when trend quality is inadequate. Knothe parameters require mine geometry, geology and measured calibration. An independent ESP32 threshold path provides node buzzer/LED indication even if RF, ML or backend fails. Gateway threshold relay needs power and received readings; node alarm is the fallback during link failure. Sources: https://doi.org/10.24425/gsm.2023.148164
https://www.issmge.org/uploads/publications/1/39/1965_02_0116.pdf
https://doi.org/10.3313/jls1964.22.2_8
https://www.dot.gov.in/static/uploads/2025/07/84f33f09e137fa81930f44bcd5f2d238.pdf

## Slide 4
TEAM
MineNova6
FEASIBILITY AND VIABILITY
@SIH Idea submission- Template
4
❖ Analysis of Feasibility, Potential Challenges & Overcoming Engineering Strategies
CHALLENGES ABOVE UNDERGROUND PANELS
Harsh surface conditions: Coal dust, monsoon rain, temperature variation, vegetation and machinery traffic affect nodes and anchors.
Surface radio obstructions: Terrain and buildings can interrupt links. Remote locations may lack cellular coverage.
False alarms and missed events: Traffic vibration, sensor drift and abrupt ground failure challenge classification and trend estimation.
Power and maintenance: Solar availability, relay duty and mesh forwarding affect energy use. Anchors and sensors need inspection.
ENGINEERING STRATEGIES & VALIDATION
Weather protection: Gasketed enclosure and hydrophobic vent. Dust/water ingress performance requires enclosure testing.
Resilient mesh: Node IDs, forwarding, acknowledgements and retries. Local ring buffers reduce data loss during outages.
Alarm robustness: Filtering, multi-sensor agreement and configurable persistence reduce nuisance alarms. Independent thresholds and watchdogs remain active.
Solar-assisted low power: Duty scheduling and replaceable battery. Autonomy requires measured sensing, forwarding and alarm power validation.
ESTIMATED PROTOTYPE NODE COST
₹2,100 / node: Planning estimate, pending itemized BOM validation. Gateway, installation and deployment costs assessed separately.
SCALABLE STUDENT PROTOTYPE
Modular deployment: Readily available ESP32/sensor modules. Site-specific anchors and baseline surveys. Validate airtime before adding nodes.
FIELD SERVICEABILITY
Replaceable components: Modular sensors, battery and enclosure. Scheduled calibration and maintenance. Service life requires field testing.
Notes: ₹2,100 is the original proposal’s estimated prototype node cost, not a verified quotation or complete system cost. Validate an itemized BOM including sensing, radio, power and enclosure before procurement. Measure energy consumption under sensing, relay, retransmission and alarm load. Buffer duration depends on storage capacity and record size. Weather rating and operating range require tests. Deployment costs include gateway, anchors, survey/calibration, installation and maintenance. Source: https://www.dot.gov.in/static/uploads/2025/07/84f33f09e137fa81930f44bcd5f2d238.pdf

## Slide 5
TEAM
MineNova6
IMPACT AND BENEFITS
@SIH Idea submission- Template
5
❖ Expected Benefits, Prototype Validation & Monitoring Support
1. COMMUNITY & WORKER SAFETY
Earlier indication: Detect developing surface movement above underground coal panels to support operator response.
Offline warning: Local siren is the primary alert. Connected gateways can send secondary SMS/app notifications.
Safer observation: Reduce routine exposure of survey crews. Ground surveys and site response plans remain necessary.
Honest warning limits: No guaranteed evacuation lead time. Abrupt failures may lack a useful precursor trend.
2. INFRASTRUCTURE & AFFORDABILITY
Risk visualization: GIS overlays measured deformation and interpreted risk zones near roads, railways and utilities.
Operational decisions: Trend histories help prioritize inspection and mitigation by qualified mine personnel.
Low-cost coverage: Estimated prototype node BOM supports a dense pilot network using accessible hardware.
Comparable budgeting: Compare complete deployments with equivalent coverage and performance after validation.
3. LAND & ENVIRONMENTAL MONITORING
Surface crack tracking: Help identify locations requiring investigation and approved remedial action.
Sensitive land uses: Monitor movement near agricultural land, forests and water infrastructure above mine panels.
Monitoring evidence: Support environmental assessment. Sensors alone cannot prevent fires, aquifer damage or subsidence.
4. REPORTING & DEPLOYMENT READINESS
Regulatory support: Designed to support monitoring/reporting aligned with relevant DGMS/CMR requirements.
CMR 2017: Reg. 111: Development work. Reg. 112: Depillaring operations.
Prototype evidence: ML uses controlled/simulated scenarios. Field calibration and real mine data required before deployment.
Reviewable records: Timestamped telemetry, alarms and calibration logs support review, not certified compliance.
Notes: Expected benefits require a validated deployment and trained operator response. No quantified deaths avoided, savings, evacuation lead time or compliance certification is claimed. Reporting alignment does not replace statutory duties, permission or site-specific engineering review. CMR 2017 cited by correct title and regulation headings; verify applicable amendments and permissions at deployment. Sources: https://www.dgms.gov.in/writereaddata/UploadFile/Coal_Mines_Regulation_2017_Noti.pdf
https://coal.gov.in/sites/default/files/2025-07/PIB2139495.pdf

## Slide 6
TEAM
MineNova6
RESEARCH AND REFERENCES
@SIH Idea submission- Template
6
❖ Verified Official Sources & Geotechnical Literature
[1] DGMS / Ministry of Labour & Employment (2017) The Coal Mines Regulations, 2017. Reg. 111: Development work. Reg. 112: Depillaring operations. Official Gazette text.
[2] Ministry of Coal (25 June 2025) Cabinet approval of the Revised Jharia Master Plan for fire, subsidence and rehabilitation. Release ID 2139495.
[3] Misa, R. (2023) Knothe’s theory parameters – computational models and examples of practical applications. Mineral Resources Management 39(4), 157–180. DOI: 10.24425/gsm.2023.148164.
[4] Saito, M. (1965) Forecasting the Time of Occurrence of a Slope Failure. Proceedings, 6th ICSMFE, Montréal, Vol. 2, pp. 537–541. ISSMGE archive.
[5] Fukuzono, T. (1985) A Method to Predict the Time of Slope Failure Caused by Rainfall Using the Inverse Number of Velocity of Surface Displacement. Landslides 22(2), 8–13. DOI: 10.3313/jls1964.22.2_8.
[6] Department of Telecommunications / WPC (2021) Use of Low Power Equipment in the Frequency Band 865–868 MHz for Short Range Devices (Exemption from Licence) Rules, 2021. G.S.R. 853(E), 10 December 2021.
[7] ISRO (2023) PSLV-C56 / DS-SAR Mission. Official mission description confirms all-weather, day-and-night SAR coverage.
Notes: [1] DGMS / Ministry of Labour & Employment (2017): The Coal Mines Regulations, 2017. Reg. 111: Development work. Reg. 112: Depillaring operations. Official Gazette text.
https://www.dgms.gov.in/writereaddata/UploadFile/Coal_Mines_Regulation_2017_Noti.pdf
[2] Ministry of Coal (25 June 2025): Cabinet approval of the Revised Jharia Master Plan for fire, subsidence and rehabilitation. Release ID 2139495.
https://coal.gov.in/sites/default/files/2025-07/PIB2139495.pdf
[3] Misa, R. (2023): Knothe’s theory parameters – computational models and examples of practical applications. Mineral Resources Management 39(4), 157–180. DOI: 10.24425/gsm.2023.148164.
https://doi.org/10.24425/gsm.2023.148164
[4] Saito, M. (1965): Forecasting the Time of Occurrence of a Slope Failure. Proceedings, 6th ICSMFE, Montréal, Vol. 2, pp. 537–541. ISSMGE archive.
https://www.issmge.org/uploads/publications/1/39/1965_02_0116.pdf
[5] Fukuzono, T. (1985): A Method to Predict the Time of Slope Failure Caused by Rainfall Using the Inverse Number of Velocity of Surface Displacement. Landslides 22(2), 8–13. DOI: 10.3313/jls1964.22.2_8.
https://doi.org/10.3313/jls1964.22.2_8
[6] Department of Telecommunications / WPC (2021): Use of Low Power Equipment in the Frequency Band 865–868 MHz for Short Range Devices (Exemption from Licence) Rules, 2021. G.S.R. 853(E), 10 December 2021.
https://www.dot.gov.in/static/uploads/2025/07/84f33f09e137fa81930f44bcd5f2d238.pdf
[7] ISRO (2023): PSLV-C56 / DS-SAR Mission. Official mission description confirms all-weather, day-and-night SAR coverage.
https://www.isro.gov.in/ISRO_EN/PSLVC56_DS_SAR_Mission.html?timeline=timeline
Saito/Fukuzono slope literature supports candidate trend methods, not proof of mine-subsidence forecast accuracy. The Knothe reference is a verified review of the theory rather than the unverified 1957 citation in the source deck.